Radiogrammetric Measurement Of Third Metacarpal Bone From Hand Radiogram Using
Active Contour Model
Submitted by:-
Priyanka-16CS13F

---
OVERVIEW
- Osteoporosis disease is caused by reduction in bone mass and strength.
- Diagnosis of osteoporosis is measurement of bone mineral density (BMD) using Dual X-ray Absorptiometry (DXA).
- DXA is expensive and not widely available in developing countries.
- Geometric measurements like cortical length , cortical width and thickness etc. of metacarpal bone are measured .
- In this project, I have done segmentation of third metacarpal bone from hand
  radiograph and radiogrammetric measurements using active contour model (chan-
  vese model).
- Cortical width and thickness are measured from the endosteal and
  periosteal edges of the metacarpal bone using which bone indices which help in
  diagnosis of osteoporosis can be computed.

---
ACTIVE CONTOUR METHOD
- Edge detection: The process of labelling the locations in the image where the grey level’s rate of change is high.
- Edge integration: The process of combining local and perhaps soarse and non-contiguous edge data into meaningful long edged curves for segmentation.

---
RADIOGRAMMETRY
CALCULATIONS TO BE DONE FROM THE OBTAINED SEGMENTED IMAGE
       cortical width, D
       medullary width, d
       cortical thickness, T = D − d
       cortical area, A = πT D(1 −T/D)
       length of the bone, L

---
IMAGE FITTING

---
FLOW CHART
RADIOGRAMMETRIC IMAGE
SEGMENTATION OF THIRD
METACARPEL
IMAGE ENHANCEMENT
DETECTION OF ENDOSTEAL
AND PERIOSTEAL EDGES
IMAGE DENOISING USING
 BM3D
RADIOGRAMMETIC
MEASUREMENTS
THRESHOLDING USING
NIBLACK
MANUAL CONTOUR
 PLACEMENT

---
OUTPUT-1
XOR
=

---
FINDING LENGTH & WIDTH

---
Dimentions Calculation
Pixel dimension=0.144 mm
No. of pixels in length= 429
No.0f pixels in width 36.2051
Length = 429 * 0.144 = 61.776 mm = 0.617 cm
Width = 36.2051 * 0.144 = 5.21353 mm = 0.521 cm

---
COMPARISON WITH STANDARD TABLE TO DETECT THE DISEASE
- Combined cortical thickness (CCT)
- Cortical area (CA)
- Cortical width (CW), D
- Medullary width (MW),d

---
REFERENCES
- Fully Automated Radiogrammetric Measurement of Third Metacarpal Bone from Hand Radiograph, Anu Shaju Areeckal, Sumam David S, Michel Kocher, Nikil Jayasheelan, Jagannath Kamath.
- Active Contours Without Edges, Tony F. Chan, Member, IEEE, and Luminita A. Vese